CERTIFICATE OF ANALYSIS

| Product Name |  | Lavandin Standard |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Product Code Category |  | LVN/02/45/PB Perfumery Base |  |  |  |  |  |  |  |
| Method of Production |  | Mixture of various Essential oils, Aromatic chemicals and Absolutes. |  |  |  |  |  |  |  |
| Color and Appearance |  | Light yellow to pale yellow thin mobile liquid. |  |  |  |  |  |
| Odor |  | Strongly herbaceous with fresh camphoraceous top note. |  |  |  |  |
| Country of Origin |  | India |  |  |  |  |  |  |  |  |
| Main Ingredients |  | Linalyl Acetate, Linalool, Eucalyptol , Camphor . |  |  |  |  |  |
| Density (200C) |  | 0.8978 g/cm3 |  |  |  |  |  |  |  |  |
| Refractive Index (200C) |  | 1.4588 nD |  |  |  |  |  |  |  |  |
| Optical Rotation |  | (-)2.768° |  |  |  |  |  |
| Flash Point |  | Not determined, estimated above 800 C. |  |  |  |  |  |
| Solubility |  | Insoluble in water, soluble in oils. |  |  |  |
| Stability |  | 24 months shelf life if stored properly |  |  |  |  |  |
| Storage |  | To be kept in closed container, in a dark, fresh & dry place |  |  |  |
| Safety |  | Harmful if swallowed. Avoid contact with eyes. |  |  |  |  |
| GC Profile |  | Soft copy available on www.bmvfragrances.com Hard copy available on request. |  |  |  |  |  |  |  |  |

Manufacturer			                             BMV Fragrances Pvt Ltd

J – 44, 45 & 46 Surajpur Industrial Area , Site V ,

Kasna, Greater Noida  ( UP )   India - 201308

Tel  No : +91 - 8800397839 / 8800397840

Sd/-

Furkan Ahmad

M.Sc (Chemistry) 						                     09/01/2020

For BMV Fragrances (P) Ltd.				Dated